## Slide 1: Monochromators
Mads Bertelsen, ESS DMSC

## Slide 2: Monochromators
Purpose of monochromators
McStas implementation and advise
Component overview:
    Monochromator
    Monochromator_curved
    Single_crystal
Exercise

## Slide 3: Monochromators: Braggs law
Uses crystal with certain lattice spacing d to select the approrpiate wavelength
Wave / interference phenomonem
Described with Braggs law

## Slide 4: Monochromator_flat
Simple monochromator, 2D rectangle
    Dimensions zwidth and yheight, oriented in yz plane
    Q or DM:
    Can give mosaicity and maximum reflectivity
Limited functionality, does not contain multiple scattering, or higher orders
Easy to use

## Slide 5: McStas monochromators
2D objects, no thickness
Orientation
z
x
z
x
z’
x’
COMPONENT Source() AT (0,0,0) ABSOLUTE
COMPONENT Mono() AT (0,0,1) RELATIVE Source ROTATED (0,theta,0) RELATIVE Source
COMPONENT Monitor AT (0,0,1) RELATIVE mono
COMPONENT beam = Arm() AT (0,0,0) RELATIVE mono ROTATED (0,theta,0) RELATIVE mono
COMPONENT Monitor AT (0,0,1) RELATIVE beam

## Slide 6: Monochromator_flat
Homogeneous spatial distribution
Small divergence distribution
Only first order simulated
Correlated position and divergence
Correlated divergence and energy
2D Position
2D Divergence
1D Wavelength
2D Pos Div
2D Pos Energy

## Slide 7: Monochromator_curved
Many flat monochromators, 2D rectangles
    Dimensions zwidth and yheight, NH x NV
    Q or DM:
    Can give mosaicity and maxium reflectivity
Limited functionality, but does have higher orders
Easy to use
yheight
zwidth
NH = 3 NV = 3

## Slide 8: Monochromator curved example
NH = 1
NV = 5
Higher vertical divergence
Several Bragg orders
2D Divergence
2D Position
1D Wavelength
2D Pos div

## Slide 9: Single_crystal
Sample component that describes a single crystal with mosaicity
    Box geometry appropriate for monochromator
    Have to set crystal parameters (other reflections available)
    Simulates transmission and absorption
Simulates multiple scattering and higher orders of Braggs laws
Not as easy to use
Have to set up focusing by using many of these together!
Will be explained in tomorrows sample session

## Slide 10: Monochromator exercise
Add a monochromator_curved after your guide from previous exercise
    Use orders = 0 to simulate all orders of Braggs law
Define selected wavelength as input parameter
Calculate theta angle for monochromator in initialize section
Remember extra arm to define new beam direction
Confirm that multiple orders are observed in the output
Extra tasks
    Experiment with focusing parameters, NH, NV, RV, RH
    Experiment with the distance between guide and monochromator