McStas introduction
DTU Physics
Sources and Monitors
part 2.

---
Sources: Source model overview
Mathematical:
Source_simple.comp
Source_div.comp
Pulsed sources:
ESS_butterfly.comp
ESS_moderator.comp
Moderator.comp
SNS_source.comp (*)
SNS_source_analytic (*)
ViewModISIS (*)
ISIS_moderator.comp (*)
Reactors :
Source_Maxwell_3.comp
Source_gen.comp
Source_gen4.comp
Source_multi_surfaces.comp (*)
I/O mechanisms:
MCPL_input/output.comp
Virtual_input/output.comp
Virtual_mcnp_ss_input/output.comp
Virtual_tripoli4_input/output.comp
Vitess_input/output.comp

---
Sources: Source_Maxwell_3
COMPONENT source = Source_Maxwell_3(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12,
T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Parameters from the PSI cold source
Initial position and direction: as for Source_simple

---
Sources: Source_Maxwell_3
COMPONENT source = Source_Maxwell_3(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12,
T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Parameters from the PSI cold source
Intensity at a given wavelength drawn from a sum of (up to) 3 normalized Maxwellian distributions:
M( %lambda, T_i ) = 2 %alpha^2 exp( - {%alpha} over {%lambda^2} ) / %lambda^5;
I( %lambda ) = sum_{ i in {1,2,3} } I_i M( %lambda, T_i );
%alpha = 949.0 K AA^2 / T_i

---
Sources: Source_Maxwell_3
COMPONENT source = Source_Maxwell_3(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12,
T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Parameters from the PSI cold source

---
Sources: Source_Maxwell_3
COMPONENT source = Source_Maxwell_3(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12,
T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Parameters from the PSI cold source
Just for fun – let’s see what happens if we remove the fast peak…

---
Sources: Source_Maxwell_3
COMPONENT source = Source_Maxwell_3(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12,
T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Parameters from the PSI cold source
Just for fun – let’s see what happens if we remove the fast peak…

---
Sources: Source_gen (Source_gen4)
COMPONENT source = Source_gen(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12,
T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Almost the same as Source_Maxwell_3: but with optional flux-files as input.

---
Sources: Source_gen (Source_gen4)
COMPONENT source = Source_gen(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12,
T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Almost the same as Source_Maxwell_3: but with optional flux-files as input.

---
Sources: Source_gen (Source_gen4)
COMPONENT source = Source_gen(yheight=0.156, xwidth=0.126,
flux_file=”file1.dat”, xdiv_file=”file2.dat”, ydiv_file=”file3.dat”)
Almost the same as Source_Maxwell_3: but with optional flux-and divergence-files as input.
Source_gen4: Same as for Source_gen but more accurate tail-description for PSI.
To generate files – e.g.
Monitor_nD(options="auto lambda per cm2", filename=”file1.dat”)
Monitor_nD(options="x hdiv, all auto", filename=”file2.dat”)
Monitor_nD(options="y vdiv, all auto", filename=”file3.dat”)

---
Sources: Source_gen (Source_gen4)
COMPONENT source = Source_gen(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12,
T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Almost the same as Source_Maxwell_3: but with optional flux-files as input.

---
Sources: Pulsed sources
Simplest case:
Use a continuous source!
Model a source with given wavelength and spatial distribution
and
… an infinitely short pulse length. I.e. t = 0 for all neutron rays.
COMPONENT src = Source_simple(
radius=0.05, lambda0=2.5, dlambda=1.5,
focus_xw=0.1, focus_yh=0.1, dist=5 )
AT(0,0,0) RELATIVE origin

---
Sources: Pulsed sources
Add a sample here TOF_monitor.
Simplest case:
Use a continuous source!
Model a source with given wavelength and spatial distribution
and
… an infinitely short pulse length. I.e. t = 0 for all neutron rays.
COMPONENT src = Source_simple(
radius=0.05, lambda0=2.5, dlambda=1.5,
focus_xw=0.1, focus_yh=0.1, dist=5 )
AT(0,0,0) RELATIVE origin

---
Pulsed Sources:
Simplest case:
Use a continuous source!
Model a source with given wavelength and spatial distribution
and
… an infinitely short pulse length. I.e. t = 0 for all neutron rays.
COMPONENT src = Source_simple(
radius=0.05, lambda0=2.5, dlambda=1.5,
focus_xw=0.1, focus_yh=0.1, dist=5 )
AT(0,0,0) RELATIVE origin
Or: Use a chopper
(Wednesday)

---
Pulsed Sources: Moderator
A flat pulsed source with uniform energy spectrum:
x in U [ - {{xwidth} over {2}} , {xwidth} over {2} ]```` y in U [ - {{yheight} over {2}}, {yheight}over{2} ] newline
lline v rline = f( %lambda ) `; %lambda in U[ L_{min} L_{max} ] newline
Time structure is given by energy dependent probability density function:
f_t = {1} over {%tau} ` exp(-{{t} over {%tau}})
%tau` =` left lbrace matrix{ t_0; # E < E_c ## t_0 left ( {1} over { 1+ {{(E-E_c)} over {%gamma}} } right ) ; #```E >= Ec } right none

---
Pulsed Sources: SNS_source
Samples directly from tallies coming from e.g. MCNP target+moderator calculations.
Originally from SNS but also used extensively at J-PARC
Can be used (with the proper input files) to model CSNS-source.
Example (coming from you) is expected to be included in next release of McStas.

---
Pulsed Sources: SNS_source
Samples directly from tallies coming from e.g. MCNP target+moderator calculations.
Can be used (with the proper input files) to model CSNS-source.
Example (coming from you) is expected to be included in next release of McStas.

---
Pulsed Sources: SNS_source_analytic
Samples from fits of Padé-functions to tallies from SNS_source.
- Requires a complex fitting campaign
+ Much faster than SNS_source
+ “Cleaner” distributions where statistics are sketchy
Can be used (with the proper input files) to model CSNS-source.

---
Pulsed Sources: ViewModISIS
Samples directly from tallies coming from e.g. MCNP target+moderator calculations.
Data file supplied for each beam port at ISIS.

---
Pulsed Sources: ViewModISIS
ISIS T2: IMAT
Samples directly from tallies coming from e.g. MCNP target+moderator calculations.
Data file supplied for each beam port at ISIS.

---
Monitors (some)
1D
L_monitor →
TOF_monitor →
Hdiv_monitor →
MeanPolLambda →
E_monitor →
2D
PSD_monitor →
PSD_monitor_4PI →
PolLambda_monitor →
Divergence_monitor →
DivPos_monitor →
nD
Monitor_nD →
I( %lambda )
I( x,y)
I( X )
I( t )
I( %theta, %phi)
or
I( ital {"div."}_x )
I ( bar bold P, %lambda )
I( X, Y)
or
langle bar bold P rangle ( %lambda )
I ( ital {"div."}_x, ital {"div."}_y )
Z ( X, Y, Z)
I( E )
I ( ital{"div."}_x, x )
or ...

---
Monitors: Quick examples
COMPONENT my_L_monitor = L_monitor(xwidth=0.2, yheight=0.2,
        nL=20, filename="Output.L", Lmin=2, Lmax=10)

---
In a histogram sense_clipboard0
In a histogram sense
Imagine a histogram, e.g. I(λ)
The RMS variance over that set becomes our statistical error bar E
In bin i, N events each carrying a fractional intensity pj so that
…
…
1
2
3
i
k

---
In a histogram sense
In a histogram sense
Monitors: Quick examples
Statistics computed on the fly
Imagine a histogram, e.g. I(λ)
The RMS variance over that set becomes our statistical error bar E
I
E
N
In bin i, N events each carrying a fractional intensity pj so that
…
…
1
2
3
i
k
# Events
Intensity / n/s
1st and 2nd moments of data
Estimated RMS MC error

---
In a histogram sense
Monitors: Quick examples
Statistics computed on the fly
Imagine a histogram, e.g. I(λ)
The RMS variance over that set becomes our statistical error bar E
I
E
N
In bin i, N events each carrying a fractional intensity pj so that
…
…
1
2
3
i
k
# Events
Intensity / n/s
1st and 2nd moments of data
Estimated RMS MC error
Statistics also available per bin (inside data file)

---
Monitors: Quick examples
In 2D
1st and 2nd moments

---
From "Virtual experiments - the ultimate aim of neutron ray-tracing simulations", K. Lefmann et al., Journal of Neutron Research 16, 97-111 (2008)

---
From "Virtual experiments - the ultimate aim of neutron ray-tracing simulations", K. Lefmann et al., Journal of Neutron Research 16, 97-111 (2008)

---
Sketch of an algorithm…
Sketch of an algorithm…
1. On a given McStas histogram
2. For the non-zero bins, calculate
   The smallest defines the “maximal counting time” allowed by your statistics
3. Preferably a “background” should be added - use a “known experimental value” or an estimate…