McStas introduction
DTU Physics
Sources and Monitors

---
Sources: In general
- A source component generates Monte Carlo neutrons.
  In McStas terms this means:
  - Set the neutron state to something representative of the source we are trying to model.
  - i.e.: insert values in the neutron state vector {x,y,z, vx,vy,vz, t, sx,sy,sz, p} drawn from appropriate distributions.
    EXAMPLE:
    Neutrons from a uniform wavelength distribution emerging from a circular aperture.

---
Access the docs
IMPORTANT:
All (and more) of this information can be found in the online pdf component documentation, e.g.http://www.mcstas.org/documentation/manual/mcstas-2.5-components.pdf
- also distributed with your McStas installation - mcdoc -c
The component documentation along with the command:
“mcdoc <component_you_are_searching_for>”
are your best friends when using McStas

---
Sources: Example 1
x in U[ -R, R ];` y in U[ -R, R ];` where x^2 + y^2 < R
Neutron spatial coordinates are picked from a uniform distribution on a circle with radius R.

---
Sources: Example 1
Length of the velocity vector encodes the wavelength
\lambda_1 \in U\left[ 1,4 \right] %lambda_1 in U [ 1,4 ] ` ` drarrow ` ` lline bold v_1 rline = f( %lambda_1 ) %lambda_2 in U [ 1,4 ] ` ` drarrow ` ` lline bold v_2 rline = f( %lambda_2 ) %lambda_3 in U [ 1,4 ] ` ` drarrow ` ` lline bold v_3 rline = f( %lambda_3 )

---
Sources: Example 1
Neutron velocity vector is picked to point at a ROI.
In McStas: this is defined by the parameters: focus_xw, focus_yh, and
dist
dist
focus_xw
focus_yh

---
Sources: Example 1
TRACE
COMPONENT origin = Progress_bar()
AT(0,0,0) ABSOLUTE
COMPONENT src = Source_simple(
radius=0.05,	lambda0=2.5, dlambda=1.5,
focus_xw=0.1, focus_yh=0.1, dist=5)
AT(0,0,0) RELATIVE origin

---
Monitors: in general
SIMULATIONS (McStas):
In McStas:
We can program monitors and detectors to behave any way we like. We refer to both of those indistinguishably as ‘monitors’.
E.g. monitor with Efficiency =100% and Transparency=100%
(With exception of PSD_Detector that models a “physical” He3 detector)
REALITY:
Monitors:
Intensity probe of the beam
Transparent to neutrons → Efficiency <1%
Detectors:
Should detect all neutrons → Efficiency as high as possible

---
Monitors: Example PSD_monitor

---
Monitors: Example PSD_monitor
When the simulation has been completed, the detected intensity in pixel (i,j) is:
I( i,j ) = sum from{x_k,y_k in pixel (i,j)} p_k; k=ray number.
… during simulation, the pixels are maintained as running sums.

---
Monitors: Example PSD_monitor and L_monitor
...
TRACE
COMPONENT origin = Progress_bar()
AT(0,0,0) ABSOLUTE
COMPONENT src = Source_simple(
radius=0.05,	lambda0=2.5, dlambda=1.5,
focus_xw=0.1, focus_yh=0.1, dist=5)
AT(0,0,0) RELATIVE origin
COMPONENT psd = PSD_monitor(
xwidth=0.2, yheight=0.2, filename=”psd.dat”)
AT (0,0,5) RELATIVE src
COMPONENT lm = L_monitor(
xwidth=0.2, yheight=0.2, filename=”lm.dat”,
Lmin=0, Lmax=8)
AT (0,0,5+0.01) RELATIVE src

---
Example 1: Results

---
Example 1: Results

---
Example 1: Results

---
Example 1: Results
If we move the PSD_monitor close to the src...

---
Monitors: information content

---
Sources: Mathematical sources
Source_simple:
Square or circular surface emitting neutrons from either uniform or Gaussian wavelength (or energy) distribution.
Neutrons are directed towards a square target.
Source_div:
Square surface emitting neutrons from either uniform or Gaussian wavelength (or energy) distribution.
Neutrons have a divergence defined by either uniform or Gaussian distribution.

---
Source_simple docs
Try “mcdoc Source_simple”
or
( in GUI ) Help → mcdoc Component Reference → (In Webpage ) Source_simple

---
Source_simple docs
Try “mcdoc Source_simple”
or
( in GUI ) Help → mcdoc Component Reference → (In Webpage ) Source_simple
Click “Input parameters”

---
Source_simple docs
Try “mcdoc Source_simple”
or
( in GUI ) Help → mcdoc Component Reference → (In Webpage ) Source_simple

---
Example 1: Results revisited
COMPONENT src = Source_simple(
radius=0.05, lambda0=2.5, dlambda=1.5,
focus_xw=0.1, focus_yh=0.1, dist=5 )
AT(0,0,0) RELATIVE origin

---
Example 1: Results revisited
COMPONENT src = Source_simple(
radius=0.05, lambda0=2.5, dlambda=1.5,
focus_xw=0.1, focus_yh=0.1, dist=5 )
AT(0,0,0) RELATIVE origin

---
Example 1: Results revisited
COMPONENT src = Source_div(
xwidth=0.1, yheight=0.1, lambda0=2.5, dlambda=1.5,
focus_aw=1, focus_ah=1, gauss=1 )
AT(0,0,0) RELATIVE origin

---
Sources: Source model overview
Mathematical:
Source_simple.comp
Source_div.comp
Pulsed sources:
ESS_butterfly.comp
ESS_moderator.comp
Moderator.comp
SNS_source.comp (*)
SNS_source_analytic (*)
ViewModISIS (*)
ISIS_moderator.comp (*)
Reactors :
Source_Maxwell_3.comp
Source_gen.comp
Source_gen4.comp
Source_multi_surfaces.comp (*)
I/O mechanisms:
MCPL_input/output.comp
Virtual_input/output.comp
Virtual_mcnp_ss_input/output.comp
Virtual_tripoli4_input/output.comp
Vitess_input/output.comp

---
Sources: Source_Maxwell_3
COMPONENT source = Source_Maxwell_3(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12,
T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Parameters from the PSI cold source
Initial position and direction: as for Source_simple

---
Sources: Source_Maxwell_3
COMPONENT source = Source_Maxwell_3(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12,
T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Parameters from the PSI cold source
Intensity at a given wavelength drawn from a sum of (up to) 3 normalized Maxwellian distributions:
M( %lambda, T_i ) = 2 %alpha^2 exp( - {%alpha} over {%lambda^2} ) / %lambda^5;
I( %lambda ) = sum_{ i in {1,2,3} } I_i M( %lambda, T_i );
%alpha = 949.0 K AA^2 / T_i

---
Sources: Source_Maxwell_3
COMPONENT source = Source_Maxwell_3(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12,
T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Parameters from the PSI cold source

---
Sources: Source_Maxwell_3
COMPONENT source = Source_Maxwell_3(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12,
T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Parameters from the PSI cold source
Just for fun – let’s see what happens if we remove the fast peak…

---
Sources: Source_Maxwell_3
COMPONENT source = Source_Maxwell_3(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12,
T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Parameters from the PSI cold source
Just for fun – let’s see what happens if we remove the fast peak…

---
Sources: Source_gen (Source_gen4)
COMPONENT source = Source_gen(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12,
T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Almost the same as Source_Maxwell_3: but with optional flux-files as input.

---
Sources: Source_gen (Source_gen4)
COMPONENT source = Source_gen(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12,
T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Almost the same as Source_Maxwell_3: but with optional flux-files as input.

---
Sources: Source_gen (Source_gen4)
COMPONENT source = Source_gen(yheight=0.156, xwidth=0.126,
flux_file=”file1.dat”, xdiv_file=”file2.dat”, ydiv_file=”file3.dat”)
Almost the same as Source_Maxwell_3: but with optional flux-and divergence-files as input.
Source_gen4: Same as for Source_gen but more accurate tail-description for PSI.
To generate files – e.g.
Monitor_nD(options="auto lambda per cm2", filename=”file1.dat”)
Monitor_nD(options="x hdiv, all auto", filename=”file2.dat”)
Monitor_nD(options="y vdiv, all auto", filename=”file3.dat”)

---
Sources: Source_gen (Source_gen4)
COMPONENT source = Source_gen(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025, focus_yh = 0.12,
T1=150.42, I1=3.67E11, T2=38.74, I2=3.64E11, T3=14.84, I3=0.95E11)
Almost the same as Source_Maxwell_3: but with optional flux-files as input.

---
Sources: Pulsed sources
Simplest case:
Use a continuous mathematical source and add time dependence:
COMPONENT src = Source_simple(
radius=0.05, lambda0=2.5, dlambda=1.5,
focus_xw=0.1, focus_yh=0.1, dist=5 )
AT(0,0,0) RELATIVE origin
EXTEND
%{
t=rand01()*1e-6;
%}

---
Sources: Pulsed sources
Simplest case:
Use a continuous mathematical source and add time dependence:
COMPONENT src = Source_simple(
radius=0.05, lambda0=2.5, dlambda=1.5,
focus_xw=0.1, focus_yh=0.1, dist=5 )
AT(0,0,0) RELATIVE origin
EXTEND
%{
t=rand01()*1e-6;
%}
Or: Use a chopper

---
Sources: SNS_source

---
Sources: ViewModISIS

---
Sources: ESS_butterfly

---
Monitors (some)
1D
- L_monitor →
- TOF_monitor →
- Hdiv_monitor →
- MeanPolLambda →
- E_monitor →
2D
- PSD_monitor →
- PSD_monitor_4PI →
- PolLambda_monitor →
nD
- Monitor_nD
I( %lambda )
I( x,y)
I( X )
I( t )
I( %theta, %phi)
or
I( divergence_x )
I ( bar bold P, %lambda )
I( X, Y)
langle bar bold P rangle ( %lambda )
or
I( E )
Z ( X, Y, Z)
or ...

---
Monitors: Quick examples
COMPONENT my_L_monitor = L_monitor(xwidth=0.2, yheight=0.2,
        nL=20, filename="Output.L", Lmin=2, Lmax=10)

---
Monitors: Quick examples
Statistics computed on the fly
# Events
Intensity / n/s
1st and 2nd moments of data
Estimated RMS MC error on Intensity