## Slide 1: SPLIT, EXTEND, WHEN, COPY & GROUP (… and the dangerous JUMP)
Advanced language features 2:

## Slide 2: Syntax in one, complex view...
{SPLIT} COMPONENT name = comp(parameters) {WHEN condition}
AT (...) [RELATIVE [reference|PREVIOUS] | ABSOLUTE]
{ROTATED {RELATIVE [reference|PREVIOUS] | ABSOLUTE} }
{GROUP group_name}
{EXTEND C_code}
{JUMP [reference|PREVIOUS|MYSELF|NEXT] [ITERATE number_of_times | WHEN condition] }

## Slide 3: SPLIT
Increase statistics beyond this point in the instrumentfile
SPLIT n MyArm = Arm()
AT somewhere
will “formulate an if-statement”:
for j=1:n
comp1
comp2
comp3
...
end (of instrument)
ONLY meaningful in case of Monte Carlo choices after SPLIT point...

## Slide 4: SPLIT
Increase statistics beyond this point in the instrumentfile
SPLIT n MyArm = Arm()
AT somewhere
will “formulate an if-statement”:
for j=1:n
comp1
comp2
comp3
...
end (of instrument)
ONLY meaningful in case of Monte Carlo choices after SPLIT point...

## Slide 5: Problem: McStas Single_crystal.comp “slow” for large unit cell diffraction studies
Example: Rubredoxin
  Reflection list ~ 124 K reflections (still “small” in the PX world!!)
slight sidetrack….

## Slide 6: Algorithm improvement: Use incoming neutrons more efficiently - scatter each one on all possible reflections
Red: Original algorithm, one incoming neutron used only once
Blue: Improved algorithm, each incoming neutron scattered (via SPLIT keyword) all possible times
Component makes estimate on average number of “active” diffraction spots - in the case Rubredoxin this is around 50!
slight sidetrack….

## Slide 7: GROUP - components working in parallel
  COMPONENT Mono1 = Monochromator_curved(...)
  AT (0,0,-LMM) RELATIVE Cradle ROTATED (0,A1/2,0) RELATIVE Cradle
  GROUP IN6Monoks
  COMPONENT Mono2 = Monochromator_curved(...)
  AT (0,0,0) RELATIVE Cradle ROTATED (0,A2/2,0) RELATIVE Cradle
  GROUP IN6Monoks
  - One comp after the other is “tried” in sequential order until the neutron was SCATTERED.

## Slide 8: EXTEND
Enrich component behaviour using EXTEND:
COMPONENT Mono1 = Monochromator_curved(...)
AT (0,0, -LMM) RELATIVE Cradle ROTATED (0,A1/2,0) RELATIVE Cradle
GROUP IN6Monoks
EXTEND
%{
if (SCATTERED) { myvar = 1; }
%}
...
COMPONENT Mono2 = Monochromator_curved(...)
AT (0,0, 0) RELATIVE Cradle ROTATED (0,A2/2,0) RELATIVE Cradle
GROUP IN6Monoks
%{
if (SCATTERED) { myvar = 2 ;}
%}
K & R. / GNU

## Slide 9: WHEN
Syntax:
COMPONENT Mine = Yours(blah, blah)
WHEN (c-expression) AT (....)
Is very powerful when combined with EXTEND and user variables, or as a method to let input parameters select if certain components are active.
Example: Use EXTEND to flag if neutron was scattered on one monochromator blade or another. Then later use WHEN to only show contribution from blade N at sample position?
COMPONENT Mon = PSD_monitor(...)
WHEN (myvar==1) AT (0,0,0) RELATIVE Sample
K & R. / GNU

## Slide 10: JUMP
A goto. Be careful. Can be used in two situations:
JUMP to myself
JUMP to an Arm
No coordinate transformations are applied... (Meaning that if the Arms you JUMP between do not coincide you will “move” / “reorient” the neutrons...)
Syntaxes:
COMPONENT a=b(...)
WHEN (expr) AT (...) JUMP somewhere
COMPONENT a=b(...)
WHEN (expr) AT (...) JUMP myself
Van Halen...

## Slide 11: JUMP
A goto. Be careful. Can be used in two situations:
JUMP to myself
JUMP to an Arm
No coordinate transformations are applied... (Meaning that if the Arms you JUMP between do not coincide you will “move” / “reorient” the neutrons...)
Syntaxes:
COMPONENT a=b(...)
WHEN (expr) AT (...) JUMP somewhere
COMPONENT a=b(...)
WHEN (expr) AT (...) JUMP myself
Van Halen...
BEWARE - This IS a GOTO!

## Slide 12: JUMP
A goto. Be careful. Can be used in two situations:
JUMP to myself
JUMP to an Arm
No coordinate transformations are applied... (Meaning that if the Arms you JUMP between do not coincide you will “move” / “reorient” the neutrons...)
Syntaxes:
COMPONENT a=b(...)
WHEN (expr) AT (...) JUMP somewhere
COMPONENT a=b(...)
WHEN (expr) AT (...) JUMP somewhere
Van Halen...
BEWARE - This IS a GOTO!

## Slide 13: COPY- inside instruments
In instruments: (see ILL_H25.instr)
COMPONENT H25_1 = Guide_gravity(
w1=0.03, h1=0.2, w2=0.03, h2=0.2, l=L_H25_1,
R0=gR0, Qc=gQc, alpha=gAlpha, m=m, W=gW)
AT (0,0,Al_Thickness+gGap) RELATIVE PREVIOUS
ROTATED (0,Rh_H25_1,0) RELATIVE PREVIOUS
COMPONENT COPY(H25_1) = COPY(H25_1)
AT (0,0,L_H25_1+gGap) RELATIVE PREVIOUS
ROTATED (0,Rh_H25_1,0) RELATIVE PREVIOUS
COMPONENT COPY(H25_1) = COPY(H25_1)(W=2*gW)
AT (0,0,L_H25_1+gGap) RELATIVE PREVIOUS
ROTATED (0,Rh_H25_1,0) RELATIVE PREVIOUS