## Slide 1: Modify a component - different hacks toward a CSNS source
  Peter Willendrup

## Slide 2: 3 approaches to try - pick which one you prefer:
Add a time-structure to Source_Maxwell_3 in an EXTEND block
Properly edit a copy of Source_Maxwell_3 and add a time structure
Add a spectrum (i.e. 1-3 Maxwellians) to the Moderator component

## Slide 3: Further work
Use the GPPD instrument file and the CSNS decoupled hydrogen input file from https://github.com/McStasMcXtrace/Schools/tree/master/CSNS_March_2019/Other and measure the spectrum
Fit 1-3 Maxwellians using iFit - use these with one of the proposed modified components
A “proper” solution for the future would be neutronics calculations for the different CSNS moderators, and characterise/fit these using Ikeda-Carpenter functions for the different time-steps, followed by “stitching” these using e.g. Padé functions in the time-domain. See attached report from SNS for examples.

## Slide 4: A “quick and dirty” temporary solution
Generate MCPL files from Vitess 3.4 and use these with McStas
Advantage:
  Straightforward and quick to do
Disadvantage:
  Slower than an analytical solution, big files, statistically limited